## Slide 1: Lecture 7: Software Defined Networks
CS5229 Advanced Computer Networks

## Slide 2: Thank you for filling up the Midterm Survey

## Slide 3: Highlights of Midterm Survey
55% have no idea what is going on half the time
25% think the lectures are pretty good
42% have not done networking before! 

## Slide 4: Good
Generally positive remarks about lecture
- enthusiastic, interesting, can learn a lot

## Slide 6: Good
Generally positive remarks about lecture
- enthusiastic, interesting, can learn a lot
“can follow if I read the papers before class.”
“I like the focus on context, would be great if this is brought up every time as we learn something new to connect the dots.”

## Slide 7: Good
Most student think that the trainings are good! 
Some think they are hard
Some think they are easy
Many students think that the programming assignments are good
Some think they are too hard

## Slide 8: Bad
Too much congestion control
Too much material/workload
Hard to understand the papers
Too fast
Not sufficiently industry-oriented
Complaints about Floodlight documentation

## Slide 9: Ugly (Suggestions)
“I hope we can cover topics which are more practical to our future work(software engineering related). Maybe something like gRPC?”
“Can we get the slides before the lecture?”
“I don't like choice questions. Can it change to a short critique for each paper?”
“Can the slides have more details?”

## Slide 10: Thank You
Many appreciate that this is a new course.
Many appreciate that it is difficult to balance between parttime students and fulltime students.
Lack of background

## Slide 11: Expectation Management
CS5229 is not an undergrad course
NUS is not a polytechnic vocation institute
CS5229 is meant to breach the gap between undergrad and PhD research
(similar to equivalent courses at top schools)
Details actually don’t matter.
Concepts matter

## Slide 12: Course Adjustments
Reduced reading list.
Week 12 Summary/Revision
Final Project: skills helpful in the industry
Made adjustments to HW + term project

## Slide 13
1st Pass
13
Title, Abstract, Intro
Read sections, sub-sections, ignore the content
Conclusion
Check out references
Triage

## Slide 14
2nd Pass
14
Look at the graphs
Mark references for future reading
Understand the key idea/ content
1 hour

## Slide 15
3rd Pass
15
Identify assumptions
Mentally re-implement the paper
Key innovation/novelty, strengths & weaknesses
Can reconstruct paper from memory/teach
You are not going to get here

## Slide 16
Quick Admin Notes
16
Questions?
Project (part-2) details will be out this weekend
AWS Credits awarded
hw-2 due on 10 Oct 23:59

## Slide 17: Plagiarism Warning
NUS’ has tightened its plagiarism policy (cheating amidst the pandemic)
Term Project
  Likely be the last assessment to be graded
  Rigorous plagiarism checks
Any instance of cheating between 2 teams:
No choice, but to FAIL THE MODULE for all 6 students

## Slide 18
Software-defined Networking

## Slide 19: The Internet: A Remarkable Story
Tremendous success
  From research experiment to global infrastructure
Brilliance of under-specifying
  Network: best-effort packet delivery
  Hosts: arbitrary applications
Enables innovation in applications
  Web, P2P, VoIP, social networks, virtual worlds
But, the change is easy only at the edge… 
Credits: Adapted from Jennifer Rexford, Princeton

## Slide 20
Inside the network, it’s a different story!

## Slide 21
To understand better, let’s take a good look at a network switch

## Slide 22: Network Switch
Front-panel Ports
Metal chassis (box)
Edgecore Wedge100BF-32X

## Slide 23: What’s inside a network switch?
Edgecore Wedge100BF-32X
Switching Chip (ASIC)
Dataplane
Match-action tables
Processes almost all traffic in/out of front-panel ports (performs “forwarding” function)
CPU + DRAM
Control Plane
Apps/Protocols: L2, BGP, etc.
Operating System (*nix)
ASIC driver
PCIe Bus
Front-panel Ports

## Slide 24: Logical view of a (traditional) Network Switch
Credits: Adapted from Nick Mckeown, Stanford/Intel
Millions of lines
of source code
7,000 Internet RFCs
Billions of gates
Bloated Power Hungry
Closed vendor-provided features/protocols: Routing, access control, VLANs, VPNs, …
Custom & Fixed Forwarding Hardware
Closed Interface (driver)
Closed Operating System
L2
BGP
VLAN
Custom CLI/script interface
Device/vendor specific
100s pages user manuals
DataPlane
Control Plane

## Slide 25: Inside the Network: A Different Story
Closed equipment
  Software bundled with hardware
    Vendor-lock in
    Expensive equipment
  Vendor-specific interfaces (CLI)
Over specified
  7000 Internet RFCs
  Slow protocol standardization
Few people can innovate
  Equipment vendors write the code
  Long delays to introduce new features
Credits: Adapted from Jennifer Rexford, Princeton

## Slide 26: Networks are Hard to Manage
Operating a network is expensive
  More than half the cost of a network
  Yet, operator error causes most outages
Buggy software in the equipment
  Routers with 20+ million lines of code
  Cascading failures, vulnerabilities, etc.
The network is “in the way”
  Network owners/operators who want control over their network
Credits: Adapted from Jennifer Rexford, Princeton

## Slide 27
Networks today are run by…
“Masters of Complexity”
Credits: Adapted from Nick Mckeown, Stanford/Intel

## Slide 28
BUT, complexity does exist across Computer Systems
Abstractions to the rescue!

## Slide 29: Abstractions in Computer Systems
Virtual memory: Abstract illusion of infinite, private physical memory
File system: Uniform illusion of read/write data store
Operating system: Shields user from CPU scheduling and peripheral sharing
(Traditional) Networking: ???
  Cannot simply say: “Block all inbound ssh connections”
  Think of vendor-specific CLI commands
    Often operator-led misconfigurations and outages
Credits: Adapted from Nick Mckeown, Stanford/Intel
Notes: Now, let’s look at

## Slide 30: “Modularity based on abstraction is the way things are done!”
Barbara Liskov (MIT)
Turing Award Lecture 2009
Credits: Adapted from Nick Mckeown, Stanford/Intel

## Slide 31: An abstraction for Networking
Idea behind the abstraction
  Operating system: decouple policy and mechanism
    e.g. Compiled C binary (computes 2+2=4) can run on both Intel and AMD CPUs
  Network: decouple control plane (policy) and dataplane (mechanism)
    e.g. Same (high-level) L2 learning program should run on both Cisco and Arista switches
Abstractions are made possible by open/standard interfaces
  Operating system: x86_64 instruction set (Intel, AMD processors)
  Network: ??

## Slide 32: An interface for Networking
SIGCOMM CCR 2008
First open and standard interface for networking

## Slide 33
Software-defined Networking (SDN 1.0)

## Slide 34: SDN: An early definition (2008)
A network in which the control plane is physically separate from the forwarding plane.
and
A single control plane controls several forwarding devices.
(Evolved over time)
Credits: Adapted from Nick Mckeown, Stanford/Intel

## Slide 35: SDN 1.0: Two Key Ideas
1. Decouple the switch’s control and data planes
  Centralize the control plane
2. Use a standard and open interface between the two planes

## Slide 36: A traditional network before SDN 1.0
Data plane: Packet processing
Forward, filter, buffer, mark, rate-limit, and measure packets (fast timescales: per-packet)
Cisco
Arista
Juniper
HPE
Credits: Adapted from Jennifer Rexford, Princeton
Notes: To get a high-level picture, let’s look at a traditional network before SDN 1.0

## Slide 37: A traditional network before SDN 1.0
Track topology changes, compute routes, install forwarding rules
(slow timescales: per control event )
Control plane: Distributed algorithms
Cisco
Arista
Juniper
HPE
Credits: Adapted from Jennifer Rexford, Princeton

## Slide 38: A traditional network before SDN 1.0
Track topology changes, compute routes, install forwarding rules
Control plane: Distributed algorithms
Cisco
Arista
Juniper
HPE
HPE CLI
Cisco CLI
Arista CLI
Juniper CLI
Credits: Adapted from Jennifer Rexford, Princeton Work illustrations by Storyset
Managing a traditional network
  Use different CLI to talk to different control plane apps
  Box-by-box configuration
Custom & Fixed Forwarding Hardware
Closed Interface (driver)
Closed Operating System
L2
BGP
VLAN
DataPlane
Control Plane
Notes: Recall our logical view of a network switch
- On each switch: Vendor specific control plane talking to vendor specific dataplane with a vendor specific interface (driver)

## Slide 39: SDN 1.0
Open and standard interface to the data plane (e.g., OpenFlow)
Logically-centralized open control plane
Switch Dataplane
Smart & slow
Dumb & fast
Generic APIs
Cisco
Arista
Juniper
HPE

## Slide 40: SDN 1.0
Recall: switch dataplane  switching chip
Idea of SDN: use OpenFlow protocol to talk to the dataplane
Q. Does it mean that we change the switching chips to understand OpenFlow?

## Slide 41
No! Switch vendors would not do it for various reasons.
Notes: Take years for all vendors to agree on certain protocol
network equipment vendors are understandably nervous, about opening up interfaces inside their boxes: they have spent years deploying and tuning fragile distributed protocols and algorithms, and they fear that new experiments will bring networks crashing down.
And, of course, open platforms lower the barrier-to-entry for new competitors.

## Slide 42: OpenFlow’s Practical Approach
Key Observation
  All network switches contain flow tables
    Implement L2/L3 forwarding, NAT, firewall, etc. that run at line rate
  Flow tables in each vendor’s switching chip are different
    But, match-action paradigm: match certain pkt hdrs, take certain actions
OpenFlow’s Key Idea
  Common set of matching headers and corresponding actions supported by most existing switches
  OF Protocol: msgs to manipulate flows tables using the common set
  Switch vendors only provide a software middleware:
    Translates OF msgs to vendor-specific interface between control and data planes

## Slide 43: OpenFlow’s Practical Approach
Custom & Fixed Forwarding Hardware
Closed Interface (driver)
Closed Operating System
L2
BGP
VLAN
Traditional Network Switch
Control Plane
OpenFlow Agent
Custom & Fixed Forwarding Hardware
Closed Interface (driver)
Closed Operating System
Control Plane
OpenFlow Network Switch
Centralized Control Plane
Vendor-specific
Interface (driver)
Note: The switch still remains closed. Except the OF agent’s standard interface
L2
BGP
VLAN

## Slide 44: Real world OpenFlow Network
Dataplane
Control Plane “Network Operating System (NOS)”
Control Program
Control Program
Control Program
Dataplane
Dataplane
Dataplane
Dataplane
CP Agent
CP Agent
CP Agent
CP Agent
Global Network Map
Counters/statistics
CP Agent
High-level languages: Python, Java, C++, etc.
Northbound
Interface
Southbound
Interface
Credits: Adapted from Nick Mckeown, Stanford/Intel

## Slide 45: Reconciling with SDN Programming Assignments
Dataplane
Control Plane “Network Operating System (NOS)”
Control Program
Control Program
Control Program
Dataplane
Dataplane
Dataplane
Dataplane
CP Agent
CP Agent
CP Agent
CP Agent
CP Agent
High-level language: ??
Northbound
Interface ??
Southbound
Interface ??
??
Credits: Adapted from Nick Mckeown, Stanford/Intel

## Slide 46: Working of an OpenFlow Network
Dataplane has simple packet-handling rules
  Pattern: match packet header bits
  Actions: drop, forward, modify, send to controller
  Priority: disambiguate overlapping match patterns
  Counters: #bytes and #packets
Credits: Adapted from Jennifer Rexford, Princeton
1. src=1.2.*.*, dest=3.4.5.*  drop
2. src = *.*.*.*, dest=3.4.*.*  forward(2)
3. src=10.1.2.3, dest=*.*.*.*  send to controller

## Slide 47: Unifies Different Kinds of Boxes
Router
  Match: longest destination IP prefix
  Action: forward out a link
Switch
  Match: dest MAC address
  Action: forward or flood
Firewall
  Match: IP addresses and TCP
/UDP port numbers
  Action: permit or deny
NAT
  Match: IP address and port
  Action: rewrite addr and port
Credits: Adapted from Jennifer Rexford, Princeton

## Slide 48: SDN 1.0: Full Programmability of the Control Plane
Controller Applications
Network OS
Events from switches Topology changes, Traffic statistics, unmatched arriving packets
Commands to switches (Un)install rules, Query statistics,
Send packets
Credits: Adapted from Jennifer Rexford, Princeton

## Slide 49
Usecases of SDN 1.0

## Slide 50: Dynamic Access Control
Inspect first packet of a connection
Consult the access control policy
Install rules to block or route traffic
Credits: Adapted from Jennifer Rexford, Princeton

## Slide 51: Seamless Mobility/Migration
See host send traffic at new location
Modify rules to reroute the traffic
Credits: Adapted from Jennifer Rexford, Princeton

## Slide 52: Server Load Balancing
Pre-install load-balancing policy
Split traffic based on source IP
src=0*
src=1*
Credits: Adapted from Jennifer Rexford, Princeton

## Slide 53: Network Virtualization
Partition the space of packet headers
Controller #1
Controller #2
Controller #3
10.*.*.*
20.*.*.*
30.*.*.*
Credits: Adapted from Jennifer Rexford, Princeton

## Slide 54: Benefits of Separation
Independent evolution and development
  The software control of the network can evolve independently of the hardware.
  e.g. Same L2 learning control plane app works for different switches
High-level control plane applications
  Control behavior using higher-order programs
  Debug/check behavior more easily (e.g. formal verification)

## Slide 55: Benefits of Centralization
Centralized decisions are easier to make
  e.g., OSPF (RFC 2328) 244 pages
  Distributed system part (builds consistent network 100 pages)
  Routing algorithm (Dijkstra’s algorithm 4 pages)
Logically vs. physically centralized
  Issues of a physically centralized controller?
  How to implement a logically centralized one?
    Using distributed systems principles: replication and fault-tolerance

## Slide 56: OpenFlow in the Wild
Open Networking Foundation
  Google, Facebook, Microsoft, Yahoo, Verizon, Deutsche Telekom, and many other companies
Commercial OpenFlow switches
  Intel, HP, NEC, Quanta, Dell, IBM, Juniper, …
Network operating systems
  NOX, Beacon, Floodlight, Nettle, ONIX, POX, Frenetic, OpenDayLight
Network deployments
  Data centers
  Cloud provider backbones
  Public backbones
Credits: Adapted from Jennifer Rexford, Princeton

## Slide 57: Overall impact of SDN 1.0
Simpler management
  Open, centralized and fully programmable control plane
Faster pace of innovation
  Less dependence on vendors and standards
Easier interoperability
  Compatibility only in “wire” protocols
Simpler, cheaper equipment
  Minimal software
Credits: Adapted from Jennifer Rexford, Princeton

## Slide 58: SDN 1.0 provided an abstraction for Networking
Highly simplified analogy with a CPU Operating System
OS
Any x86 CPU
(Intel, AMD, VIA, Zhaoxin)
App1
App2
AppN
x86 ISA
NOS
Any OpenFlow Switch*
(HPE, Cisco, Juniper, Arista, Brocade, etc.)
App1
App2
AppN
* Network Switch = Packet Processing Unit
OpenFlow
Final Note: SDN != OpenFlow

## Slide 59
Q. SDN has a lot of benefits. Should we deploy SDN switches everywhere?
The Internet?
Campus/Enterprise Networks?
Datacenters?

## Slide 60
Programmable Dataplanes

## Slide 61: In the Beginning…
OpenFlow was simple
A single rule table
  Priority, pattern, actions, counters, timeouts
Matching on any of 12 fields, e.g.,
  MAC addresses
  IP addresses
  Transport protocol
  Transport port numbers
  Metadata fields: ingress_port
Credits: Adapted from Jennifer Rexford, Princeton

## Slide 62: “Second System” Syndrome
OpenFlow 1.0 limitations
  One (logical) flow table
  Limited headers and actions
  Sending packets to the controller
Later version of OpenFlow
  More flow tables, headers, actions
  But, still never enough
  Where does it stop?!?
Credits: Adapted from Jennifer Rexford, Princeton
Version | Date | # Headers
OF 1.0 | Dec ‘09 | 12
OF 1.1 | Feb ‘11 | 15
OF 1.2 | Dec ‘11 | 36
OF 1.3 | Jun ‘12 | 40
OF 1.4 | Oct ‘13 | 41
OF 1.5.1 | Mar ‘15 | 44

## Slide 63: Protocol Dependence of SDN 1.0
Consider the following action types (OpenFlow 1.5.1)
  OFPAT_PUSH_VLAN = 17, /* Push a new VLAN tag */
  OFPAT_POP_VLAN = 18, /* Pop the outer VLAN tag */
  OFPAT_PUSH_MPLS = 19, /* Push a new MPLS tag */
  OFPAT_POP_MPLS = 20, /* Pop the outer MPLS tag */
  OFPAT_PUSH_PBB = 26, /* Push a new PBB service tag (I-TAG) */
  OFPAT_POP_PBB = 27, /* Pop the outer PBB service tag (I-TAG) */
OpenFlow actions are tied to specific protocols

## Slide 64: Dataplane dependence of SDN 1.0
Support VXLAN (new packet encapsulation protocol)
  VXLAN protocol requires per-packet line-rate operations
  Dataplane should first support the VXLAN protocol
    VXLAN Flow Table: match on VXLAN header fields
    Support actions: PUSH_VXLAN, POP_VXLAN, modify VXLAN
  Then extend OpenFlow protocol: manipulate VXLAN flow table
Recall: OpenFlow open/standard interface to the existing flow tables in the switch dataplane (forwarding chip/ASIC)
Switch dataplane determines ultimate limit of programmability!

## Slide 65
Q. Can we do better? Can we “program” a new protocol into the switch dataplane?

## Slide 66: Reconfigurable Match Tables (RMT)
SIGCOMM 2013
Architecture of a programmable switching chip (dataplane)
Notes: Yes! This paper, ‘forwarding metamorphosis’ made it possible. They proposed something called as the RMT

## Slide 67: P4: Programming Protocol-Independent Packet Processors
SIGCOMM CCR 2014
Domain-specific language for a programmable switching chip

## Slide 68
RMT + P4  enable a programmable dataplane (SDN 2.0)

## Slide 69: Main goal of P4: Protocol Independence
Key ideas to achieve protocol independence
  Programmable parsing: tell the chip how to parse packets
    e.g. if UDP dstPort == 4789, next header is VXLAN
  Typed match-action tables: define your own match fields
    e.g. new protocol’s header field like VXLAN ID
  Programmable actions: define your own actions
    e.g. push/pop VXLAN header, modify VXLAN ID, forward based on VXLAN ID

## Slide 70: Programmable Actions in P4
Protocol-independent actions primitives
Used to defined custom actions
P4 can support future protocols (not known today)
  More simple, elegant and future proof than OpenFlow 1.x
add_header() remove_header()
set_field() increment()
action add_vlan_hdr(){
add_header(vlan_hdr);
}
action add_vxlan_hdr(){
add_header(vxlan_hdr);
}

## Slide 71: Limitations of a programmable dataplane
High-level constraint: all processing MUST maintain line rate
No “loop” constructs
No floating point computations
  Only approximate computations possible

## Slide 72: Impact of dataplane programmability (SDN 2.0)
Protocol independence
  Faster and easier network evolution: new protocols/headers
  Traditionally new protocol addition takes 4-5 years!!
    Requires design and development of a new fixed-function switching chip
  SDN 2.0 brings this time down to weeks/months.
Flexible Resource Allocation
  Traditional switches: L2, L3, ACL, VLAN consume chip’s resources
  SDN 2.0: define only the required tables
    If using the box L3 router: just program L3 table with large # of entries
  Throw away unused tables: simplified data and control planes
    Helps reduce unwanted bugs

## Slide 73: Impact of dataplane programmability (SDN 2.0)
Reconfigurability in the field
  Traditionally, upgrading for a new protocol requires h/w upgrades
    Long and expensive downtimes. Error-prone risky task!
  SDN 2.0: Hardware upgrades  software upgrades
    Downtime: 10s-100s of ms
  Good return on investment (ROI)
    Buy a switch with a programmable chip today. Enjoy software upgrades for years to come!

## Slide 74: Dataplane Programmability in the wild
P4-programmable switching chips
  Intel Tofino, Tofino2
Commercial switches with P4-programmable switching chip
  Cisco, Arista, Edgecore, Inventec
SmartNICs
  NetFPGA, Netronome, Xilinx
P4 also used to specify software packet processing
  XDP, eBPF, OpenVSwitch
P4 has become the de-facto language to specify packet processing 

## Slide 75: Features beyond protocol independence
Queuing Telemetry Information
  Enqueue/dequeue queue depth (per-packet)
  Time spent in the queue (per-packet)
Transactional Memory (SRAM) + Stateful ALUs
  Stateful operations across multiple packets
  Simple computations: add, subtract, approx. multiply/divide
High-resolution Timestamping
  Nanosecond-scale timestamps
Packet cloning/replication
  Flexible mirroring or conditional multicasts (at run time)

## Slide 76: Value for Network Researchers
Previously
  Cannot propose a dataplane-level solution
  No way to prototype and validate. Simulations typically not accurate!
Today
  Propose a dataplane-level solution for new/existing problems in networking/systems
  P4 programmable platform: readily “realize” the solution in production hardware at full line rate (100G/400G)

## Slide 77: Hottest topic in networking Research
In-Network Computing
  In-network caching [NetCache, SOSP’17]
  In-network chain replication [NetChain, NSDI'18, Best Paper]
  In-network DDoS detection and mitigation [Jaqen, Security'21]
Programmable Packet Scheduling (AQMs)
  [SP-PIFO, NSDI’20], [Calendar Queues, NSDI’20], [AIFO, SIGCOMM’21]
Co-designing distributed systems with the network
  NOPaxos [OSDI‘16], Pegasus [OSDI’20]  Week 11
Lot more papers on network telemetry and verification
  Network verification: Both OpenFlow and P4 have opened up a whole new research area

## Slide 78: Hottest networking topic in the Industry
Google
  Using P4 to encode/specify the behavior of existing switches
    Apply formal verification techniques: check correctness of configurations
Microsoft Azure
  Protocol independence, Reconfigurability in the field (better ROI)
Kuaishou
  Translating IPv6 traffic to IPv4 and vice-versa
AliBaba
  NetSeer: tracking every single packet drop [SIGCOMM’20]
  SailFish: Multi-tenant, multi-service gateways [SIGCOMM’21]
    Already running in production
5G Usecases
  Several companies: Accelerating UPF, slicing 5G networks

## Slide 79: Networking Research using P4 @SoC
APSys’18
SOSR’19
ICNP’19
NSDI’21

## Slide 80: Networking Research using P4 @SoC

## Slide 81: Networking Research using P4 @SoC

## Slide 82: Networking Research using P4 @SoC

## Slide 83
If you are interested, reach out!

## Slide 84: Summary
Traditional Network Switches
  Completely closed, vertically integrated
  Only equipment vendors: drive the innovation and evolution
OpenFlow (SDN 1.0) made the control plane programmable
  Provided an abstraction to manage and operate networks in s/w
P4 (SDN 2.0) took the s/w programmability to the dataplane
  Made networking truly software-defined
SDN has enabled network owners and operations to take back the control of their network!