## Slide 1: EE4204 Socket Programming Assignment and Example Programs
Prepared by: Sivaraman Vignesh (Ex-Graduate Assistant)
Module Lecturer: Assoc. Prof. Mohan Gurusamy
Electrical and Computer Engineering Department
National University of Singapore

## Slide 2
Response
Request
P
O
R
T
P
O
R
T
Used to do communication between two processes running on two different machines
An object (special file) which acts as an end point between two machines
Socket | IP_Address:Port (Ex: 127.0.0.1:4950)
IP Address
IP
Address
What is socket?
Client
Server

## Slide 3: Sockets
Application Programming Interface (API)
Interface between an application and network
Application creates a socket
The interface defines the following operations
  Create a socket
  Attach a socket to the network
  Send/receive messages through a socket
  Close a socket

## Slide 4: Example 1
Develop a socket program in UNIX/Linux that uses (i) TCP as the transport protocol and (ii) UDP as the transport protocol for transferring a short message between a client and server. The client sends a string (input by the user) to the server and the server prints the string on the screen after receiving it.

## Slide 5: UDP (Connectionless)
Server
Create socket
Bind
ReceiveFrom
client
Create socket
SendTo

## Slide 6: UDP
Socket()
bind()
recv()
close socket
Socket()
send()
close socket

## Slide 7: UDP (Connectionless)
Server
Create socket
Bind
ReceiveFrom
client
Create socket
SendTo

## Slide 8
Client

## Slide 9
Client
(conti:)

## Slide 10
Header file

## Slide 11: Socket structure
 The McGraw-Hill Companies, Inc., 2000

## Slide 12: Socket – Family and Type
Socket Family
  AF_INET : Internet Family
  AF_UNIX: Unix Pipe facility
Socket Type
  SOCK_STREAM: byte stream such as TCP
  SOCK_DGRAM: message oriented service such as UDP
Protocol
  Specifies either TCP or UDP
  ‘Zero’

## Slide 13: UDP Client
Create a socket
Chosen by the system
 The McGraw-Hill Companies, Inc., 2000

## Slide 14: UDP Client
Has information like name,
aliases, address type etc
Get the server address
Server address(remote socket)
 The McGraw-Hill Companies, Inc., 2000
Send data to the server

## Slide 15: UDP
Server
Create socket
Bind
Receivefrom
client
Create socket
Sendto

## Slide 17: UDP Server
Creating socket is same as the client
Values of the other tuples
In case the system has multiple IPs
 The McGraw-Hill Companies, Inc., 2000

## Slide 18: UDP Server
Bind function: Associates the socket with the given local address
Receive from client
Client address (remote socket)
Close the socket (both at server and client)

## Slide 19: headsock.h (Ex 1)

## Slide 20: TCP (Connection-oriented)
server
Create socket
Bind
Listen
Accept
Receive/Send
client
Create socket
Connect
Send/Receive

## Slide 21: TCP
Socket()
bind()
accept()
listen()
recv() & send()
close socket
Socket()
connect()
send() & recv()
close socket

## Slide 22: TCP
server
Create socket
Bind
Listen
Accept
Receive
client
Create socket
Connect
Send

## Slide 25: Example 1 (TCP): Client
Server address (from command line)
Creating a socket and connecting to it

## Slide 26: Example 1 (TCP): Client
Client application to send a string to the server

## Slide 27: TCP
server
Create socket
Bind
Listen
Accept
Receive
client
Create socket
Connect
Send

## Slide 30: Example 1 (TCP): Server
Create a socket and bind at the server

## Slide 31: Example 1 (TCP): Server
Informs the OS, that socket is ready for requests (listen)
Connect to an incoming request (accept)
Server application to receive a string from a client

## Slide 32: Lets try example 1
Server
Run the code
  gcc tcp_ser1.c –o ser
Start Server
  ./ser
client
Run the code
  gcc tcp_client1.c –o client
Start Server
  ./client 127.0.0.1
Note:
127.0.0.1 is a loopback IP.
To find IP address of any device, use command ‘ifconfig’

## Slide 33: Example 2
Develop a TCP-based client-server socket program for transferring a large message. Here, the message transmitted from the client to server is read from a large file. The entire message is sent by the client as a single data-unit. After receiving the file, the server sends an ACK message to the receiver. Verify if the file has been sent completely and correctly by comparing the received file with the original file (“diff” command could be used). Measure the message transfer time and throughput.

## Slide 34: Example 2: Client
The TCP connection process is same as Example 1
Open the file in read mode
Determine the length of the file
Read the file into the buffer
Send the file to the server

## Slide 35: Example 2: Client
Wait for the ack
Check if it is an Ack and calculate the time taken

## Slide 37: Example 2: Server
Receive the whole file from client

## Slide 38: Example 2: Server
Send ack to client after receiving the whole file
Save the file from buffer to a file

## Slide 40: headsock.h (Ex 2)

## Slide 41: Example 3
Develop a TCP-based client-server socket program for transferring a large message. Here, the message transmitted from the client to server is read from a large file. The message is split into short data-units which are sent one by one without waiting for any acknowledgement between transmissions of two successive data-units. Verify if the file has been sent completely and correctly by comparing the received file with the original file. Measure the message transfer time and throughput for various sizes of data-units.

## Slide 42: Example 3: Client sending file in data units
Sending file in data units of size DATALEN

## Slide 43: Client waits for Ack

## Slide 45: Example 3: Server receiving file in data units
Receiving file in data units of size DATALEN

## Slide 46: Server sending Ack and saving the file
Send ack to client
Save the file from buffer to a file

## Slide 48: headsock.h (Ex 3)

## Slide 49: Assignment Problem
Develop a UDP-based client-server socket program for transferring a large message. Here, the message transmitted from the client to server is read from a large file. The message is split into short data-units (DUs) which are sent and acknowledged in batches of size 1, 2, and 3 DUs. The sender sends one DU, waits for an acknowledgment (ACK); sends two DUs, waits for an ACK; sends three DUs, waits for an ACK; and repeats the above procedure until the entire file is sent. The receiver sends an ACK after receiving a DU; sends next ACK after receiving two DUs; sends next ACK after receiving three DUs; and repeats the above procedure.

## Slide 50
Client
Server
1st transmission
2nd transmission
3rd transmission
And so on……
1st reception
2nd reception
3rd reception
And so on……
Wait for 1 packet then send ’ack’
Wait for 2 packet then send ’ack’
Wait for 3 packet then send ’ack’
1
2
3

## Slide 51: Example 4 (Assignment Problem)
Verify if the file has been sent completely and correctly by comparing the received file with the original file. Measure the message transfer time and throughput for various sizes of data-units and compare it with the stop-and-wait protocol where the batch size is always fixed to be 1. Choose appropriate values for “data unit size” and measure the performance. Repeat the experiment several times and plot the average values in a report with a brief description of results, assumptions made, etc.
Include the following performance figures in your report:
  Transfer time vs data unit size ( one curve for this problem and one curve for stop-and-wait )
  Throughput vs data unit size ( one curve for this problem and one curve for stop-and-wait )